## Slide 2: Introduction
It is 32-bit ARM Cortex-M based microcontroller family by STMicroelectronics
Performance
Low power consumption
Rich peripherals
Advanced security
Wireless connectivity

## Slide 3: STM32 Core Families
Cortex-M0/M0+
Cortex-M3
Cortex-M4
Cortex-M7
Cortex-M33/M55
STM32F0

## Slide 4: STM32 Core Families
Cortex-M0/M0+
Cortex-M3
Cortex-M4
Cortex-M7
Cortex-M33/M55
STM32F1

## Slide 5: STM32 Core Families
Cortex-M0/M0+
Cortex-M3
Cortex-M4
Cortex-M7
Cortex-M33/M55
STM32F3

## Slide 6: STM32 Core Families
Cortex-M0/M0+
Cortex-M3
Cortex-M4
Cortex-M7
Cortex-M33/M55
STM32F7

## Slide 7: STM32 Core Families
Cortex-M0/M0+
Cortex-M3
Cortex-M4
Cortex-M7
Cortex-M33/M55
STM32U5

## Slide 8: Block Diagram
STM32 CHIP
CORTEX CORE
BUS MATRIX
FLASH
PERIPHERALS
SRAM
GPIO
USART
I2C
SPI

## Slide 9: Core characteristics
32-bit processing
RISC architecture
Power efficiency
Harvard architecture
On-chip components

## Slide 10: STM32F103C8T6

## Slide 11: Specifications
Feature | STM32F103C8T6
FLASH (ROM) | 64kB/128kB
SRAM | 20kB
UART | 3
SPI | 2
I2C | 2
Timers | 7
Clock Speed | 72MHz

## Slide 12: GPIO Pin Information:
The STM32F103C8T6 microcontroller has 37 GPIO pins available, organized into 3 ports:
1-Port A (GPIO): PA0 to PA15 (16 pins)
2-Port B (GPIOB): PB0 to PB15 (16 pins)
3-Port C (GPIOC): PC13 to PC15 (3 pins)

## Slide 13: GPIO Pin
PINS | Description
PA0-PA15 | ADCI(Analog to Digital Converter) Inputs
PB0,PB1 | Additional Analog inputs
PA9(TX) | USART 1
PA10(RX) | 
PA2(TX) | USART 2
PA3(RX) | 
PB10(TX) | USART 3
PB11(RX) | 

## Slide 14
PINS | Description
PA4(CS) | SPI 1
PA5(SCK) | 
PA6(MISO) | 
PA7(MOSI) | 
PB12(CS) | SPI 2
PB13(SCK) | 
PB14(MISO) | 
PB15(MOSI) | 

## Slide 15
PINS | Description
PB6(SCL) | I2C 1
PB7(SDA) | 
PB10(SCL) | I2C 2
PB11(SDA) | 
SWDIO | Serial Wire debug input/output
SWCLK | Serial Wire Clock

## Slide 16: Blue Pill Pinout Diagram (STM32F103)

## Slide 17: Core CPU registers include
Registers | Description
R0-R12 | General-purpose registers
R13 | Stack Pointer
R14 | Link Register
R15 | Program Counter
xPSR | Program Status Register

## Slide 18: Applications:
Consumer Electronics
Industrial Automation
Robotics
Communication devices

## Slide 19: THANK YOU